## Slide 1
Do It Yourself DCC++
A full-featured DCC system using an Arduino an Arduino Motor Shield and connecting it to a model railroad for less than $100.
Presented by David Ramos
dramos_1701@yahoo.com

## Slide 2: Do It Yourself DCC++
How did we get here?
Evolution
Our first trainset
DC Block control
DC Tethered Throttles
Early Analogue Command Control
DCC – Digital Command Control

## Slide 3: Do It Yourself DCC++
Image from: http://trains4africa.co.za/?p=1451

## Slide 4: Do It Yourself DCC++
Traditional DCC Suppliers
Yes there are many others!

## Slide 5: Do It Yourself DCC++
Let’s go shopping!
Parts List:
Arduino Uno R3
Build Price:
$11.86

## Slide 6: Do It Yourself DCC++
Let’s go shopping!
Parts List:
R3 Power Shield
Build Price:
$20.82

## Slide 7: Do It Yourself DCC++
Let’s go shopping!
Parts List:
Micro SD Card
Build Price:
$26.61

## Slide 8: Do It Yourself DCC++
Let’s go shopping!
Parts List:
Power Supply 14 Volt 5 Amps
Build Price:
$40.95

## Slide 9: Do It Yourself DCC++
Let’s go shopping!
Parts List:
Jumper Wire for Arduino
Build Price:
$48.94

## Slide 10: Do It Yourself DCC++
Let’s go shopping!
Parts List:
Raspberry Pi 3 B+
Build Price:
$86.75

## Slide 11: Do It Yourself DCC++
Let’s go shopping!
Parts List:
Raspberry Pi 3 B+ Power Supply
Build Price:
$96.74

## Slide 12: Do It Yourself DCC++
Let’s go shopping!
Parts List:
Arduino Uno R3 $11.86
R3 Power Shield $5.97
Shipping $2.99
Micro SD Card $5.71
Power Supply 14 Volt 5 Amps $14.31
Jumper Wire for Arduino $7.99
Raspberry Pi 3 B+ $37.81
Raspberry Pi 3 B+ Power Supply $9.99
Build Price: $96.74
Amazon
EBay
EBay
Amazon
Amazon
Amazon
Amazon
Amazon

## Slide 13: Do It Yourself DCC++
Free Software and stuff to make it work
Arduino Programing Software
https://www.arduino.cc/en/Main/Software
GitHub – Repository of the DCC ++ Firmware for the Arduino
https://github.com/DccPlusPlus/BaseStation
JMRI – Repository for the Raspberry Pi JMRI Software
https://mstevetodd.com/jmri-raspberrypi-access-point
Windows Disk Imager – Needed to Program the Raspberry Pi
https://sourceforge.net/projects/win32diskimager/
Apple Disk Imager: ApplePi v2
https://www.tweaking4all.com/hardware/raspberry-pi/applepi-baker-v2/
NOOBS for Raspberry Pi
https://www.raspberrypi.org/downloads/noobs/

## Slide 14: Do It Yourself DCC++
Free Software and stuff to make it work
Arduino Programing Software
https://www.arduino.cc/en/Main/Software

## Slide 15: Do It Yourself DCC++
Free Software and stuff to make it work
GitHub – Repository of the DCC ++ Firmware for the Arduino
https://github.com/DccPlusPlus/BaseStation
https://github.com/DccPlusPlus/BaseStation/wiki/What-is-DCC--Plus-Plus

## Slide 16: Do It Yourself DCC++
Free Software and stuff to make it work
JMRI – Repository for the Raspberry Pi JMRI Software
https://mstevetodd.com/jmri-raspberrypi-access-point

## Slide 17: Do It Yourself DCC++
Free Software and stuff to make it work
Windows Disk Imager – Needed to Program the Raspberry Pi
https://sourceforge.net/projects/win32diskimager/

## Slide 18: Do It Yourself DCC++
Free Software and stuff to make it work
Apple Disk Imager: ApplePi v2
https://www.tweaking4all.com/hardware/raspberry-pi/applepi-baker-v2/

## Slide 19: Do It Yourself DCC++
Free Software and stuff to make it work
NOOBS for Raspberry Pi
https://www.raspberrypi.org/downloads/noobs/

## Slide 20: Do It Yourself DCC++
How to Videos on YouTube
Excellent Beginners how to guide by: Steve Todd
https://www.youtube.com/watch?v=l1pgvCKT410
More detailed four part series.
https://www.youtube.com/watch?v=-nsVdpMhiTU

## Slide 21: Do It Yourself DCC++
Starting the Build
Step 1: Install Arduino IDE on your laptop or desktop.
Step 2: Download from GitHub the DCC++ firmware for the Arduino.
Step 3: Connect the Arduino to your computer.
Step 4: Using the Arduino IDE, push the code to the Arduino
Step 5: Cut the trace on the back of the Power Shield
  This is done to protect the CPU on the Arduino since it is designed to handle 12 Volts and this project requires 14 Volts!

## Slide 22: Do It Yourself DCC++
Starting the Build
Step 6: Connect the Power Shield to the Arduino

## Slide 23: Do It Yourself DCC++
Starting the Build
Image from: http://www.motorhomesites.org.uk/dcc-arduino-with-jmri-raspberry-pi/

## Slide 24: Do It Yourself DCC++
Starting the Build
There are two jumper that you will need to put in.
Jumper #1 Pin 10 and 12
This provides the DCC Logic to be transmitted to the Mail Track Power.
Jumper #2 Pin 5 and Pin 13
This provides the DCC Logic to be transmitted to the Programing track.
The Blue USB connector needs to go to either a Computer, Laptop or a Raspberry Pi Running JMRI.
Programing
Main

## Slide 25: Do It Yourself DCC++
Starting the Build
There are two jumper that you will need to put in.
Jumper #1 Pin 10 and 12
This provides the DCC Logic to be transmitted to the Mail Track Power.
Jumper #2 Pin 5 and Pin 13
This provides the DCC Logic to be transmitted to the Programing track.
The Blue USB connector needs to go to either a Computer, Laptop or a Raspberry Pi Running JMRI.
Programing
Main

## Slide 26: Do It Yourself DCC++
JMRI
There are a few paths you can take at this point.
You can use an existing Laptop or computer to connect to the DCC++ or you can program a Raspberry Pi to do the job. Here is what goes next.
With the Laptop or desktop you will need either a router or software to turn then computer in to a wireless access point. You will need to install JMRI and set it up to talk to the DCC++ over a USB cable.

## Slide 27: Do It Yourself DCC++
JMRI
There are a few paths you can take at this point.
With the Raspberry Pi there will be some configuring task and software that you will need to do.
For this task you will need an install image to setup the Raspberry Pi. Not to worry a complete solution is available at the JMRI website. You will need the image file and a software to configure the Micro SD card.
Windows based PC should use Windows 32 Disk Imager and Mac OS users will need to use ApplePi-Baker V2.
Both of these programs take the file and convert it to a bootable file that will program the Raspberry Pi!

## Slide 28: Do It Yourself DCC++
Ready For Testing
The Wi-Fi SSID: JMRI-LVRR
Password: LVRR1925

## Slide 29: Do It Yourself DCC++
Ready For Testing
The Wi-Fi SSID: JMRI-LVRR
Password: LVRR1925

## Slide 30: Do It Yourself DCC++
What If?
If you have a DCC system like an NCE system already you can use the Raspberry Pi to add Wi-Fi throttles to your layout.
You will need a USB to Com Port male cable.

## Slide 31: Do It Yourself DCC++
Additional Boosters?
Tam Valley Depot makes and excellent Stand alone DCC booster system that will let you expand the scope of your railroad.
Booster Cost: $54.95
Power Supply: $16.95

## Slide 32: Do It Yourself DCC++
Questions?

## Slide 33: Do It Yourself DCC++
Go out and build one!